NSTX Upgrade

OH-PF1a/b Magnetic Stability

NSTXU-CALC-133-11-00

Rev 0

March 2 2011

Prepared By:

___________________________________

Peter Titus, PPPL Mechanical Engineering

___________________________________

Ali Zolfaghari,  PPPL Mechanical Engineering

Reviewed By:

________________________________________

H.M. Fan

Approved By:

________________________________________

Jim Chrzanowski, NSTX Cognizant Engineer

PPPL Calculation Form

Calculation # 	NSTXU-CALC-133-11-00    Revision #  00		WP #, 1672

(ENG-032)

Purpose of Calculation: (Define why the calculation is being performed.)

To demonstrate that the structural elements that center the centerstack are stiff enough to overcome magnetic instabilites between the OH and PF1a, and b which are mounted on the centerstack casing. This calculation has been prepared in response to a PDR CHIT.

References (List any source of design information including computer program titles and revision levels.)

[1] NSTX-CALC-13-001-00 Rev 1  Global Model – Model Description, Mesh Generation, Results, Peter H. Titus  February  2011

[2] NSTX Structural Design Criteria Document, NSTX_DesCrit_IZ_080103.doc I. Zatz

[3] NSTX Design Point June 3 2010 http://www.pppl.gov/~neumeyer/NSTX_CSU/Design_Point.html

[4] Centerstack Casing Bellows, Peter Rogoff, NSTXU-CALC-133-10-00

[5] OH Preload System and Belleville Spring Stack Design, Peter Rogoff, NSTXU-CALC-133-04-00

Assumptions (Identify all assumptions made as part of this calculation.)

The only PF interaction that was investigated was the PF1a/b -OH pairing. This is judged to be the most flexible structural interaction in the PF system because at the upper end of the casing and OH, the PF1a,and b are only stabilized by the stiffness of the bellows, and OH preload mechanism.

Calculation (Calculation is either documented here or attached)

Attached in the body of the calculation

Conclusion (Specify whether or not the purpose of the calculation was accomplished.)

The magnetic stiffness was calculated to be .637 MN/m and the structural stiffness was calculated to be 100 MN/m (Combined bellows and Belleville Spring Post Stiffness) . The structural stiffness must exceed the magnetic stiffness for the coils to be stable. - which it does with a large margin.

Cognizant Engineer’s printed name, signature, and date

Jim Chrzanowski

I have reviewed this calculation and, to my professional satisfaction, it is properly performed and correct.

Checker’s printed name, signature, and date

H.M.Fan

Table of Contents

Executive Summary	3

DCPS Input	4

Interaction Forces Due to Concentric Misalignment of Inner PF Coils with Respect to the OH Coil Using MAXWELL	4

Interaction Forces Due to Concentric Misalignment of PF1a Coil with Respect to the OH Coil	4

Interaction Forces Due to Concentric Misalignment of PF1a and PF1b Coils with Respect to the OH Coil	5

Interaction Forces Due to Concentric Misalignment of Inner PF Coils with Respect to the OH Coil using the NTFTM Code	6

Lateral Structural Stiffness - Bellows and Cantelevered Centerstack Casing	8

Compliance of the Belleville Spring Preload System	10

Executive Summary:

The possibility of magnetic instabilities of the various poloidal coils was raised at the CDR and PDR. All the coils are well supported off the  vacuum vessel or centerstack casing. There are no coils supported by light, flexible supports. PF 1a and 1b upper and lower are mounted on the centerstack casing. The radial connection between the centerstack casing and the rest of the NSTX structure is rigid and strong at the lower casing connections. A "skirt" connects the lower casing flange to the lower TF flag structures. PF1 a and b lower are aligned stiffly with respect to the OH. At the upper end there is no connection between the centerstack and the TF or the OH. Alignment is maintained by the upper bellows. The OH is also well  positioned with respect to the TF at the lower end through the "skirt", but at the upper end, alignment is maintained by the lateral stiffnesses of the belleville preload mechanism. The centerstack TF components are well centered by the spoked lid and collar.    This calculation addresses the magnetic stability of the centerstack assembly with respect to the  OH coil, Magnetic loads that result from a unit  offset of the centers of the coils are computed in MAXWELL. This establishes an Magnetic "stiffness". This is then compared with a structural stiffness. The structural stiffness must exceed the magnetic stiffness for the coils to be stable. The magnetic stiffness was calculated to be .637 MN/m and the structural stiffness was calculated to be 425 MN/m

# DCPS Input

This calculation demonstrates a large stability margin between the inner PF coils and the OH coil, with peak coil currents applied. No interface with the DCPS is required.

# Interaction Forces Due to Concentric Misalignment of Inner PF Coils with Respect to the OH Coil Using MAXWELL

Interactions between the inner PF coils and the OH due to deviations in concentricity have been evaluated using the MAXWELL code. MAXWELL is a finite element electromagnetic code used to solve electromagnetic field equations in 2d and 3D. In this analysis we have used MAXWELL 3D to obtain forces on solenoids that represent the OH, PF1a and PF1b coils in NSTX upgrade.

# Interaction Forces Due to Concentric Misalignment of PF1a Coil with Respect to the OH Coil

Coil		Current (kA)		Turns

OH		24			884	reference [3]

PF1a		18.3			64	reference [3]

PF1a and is moved from its concentric position with respect to the OH coil by two different distances of 2mm and 5 mm.

# Interaction Forces Due to Concentric Misalignment of PF1a and PF1b Coils with Respect to the OH Coil

PF1a and PF1b are moved from their concentric position with respect to the OH coil by two different distances of 2mm and 5 mm. As expected, if the currents in PF1a and PF1b are in parallel to the current in OH, once the Pf1a and PF1b are moved from their concentric orientation with respect to the OH, a force appears which is increased with the distance and tries to further the distance. This can be interpreted as resulting in a magnetic stiffness equivalent to the magnetic force divided by the distance. The table below list the computed forces vs. distance.

Setup:

Coil		Current (kA)		Turns

OH		24			884	Reference [3]

PF1a		18.3			64	Reference [3]

PF1b		13			32	Reference [3]

The PF1a and PF1b are moved together 2mm and 5mm in the positive Y direction.

| Orientation of PF1a and PF1b currents with OH current | PF1a and PF1b Offset (mm) with respect to OH in +Y direction | Total Force (N) on PF1a & PF1b in +Y Direction |
| --- | --- | --- |
| Parallel | 2 | 2124 |
| Opposite | 2 | -2140 |
| Parallel | 5 | 6099 |
| Opposite | 5 | -5579 |
| Parallel | 0 | -311 |
| Opposite | 0 | 576 |

Magnetic  Stiffness= 6000/.005 N/m =  1.274MN/m For the combined effects of PF1a,b and the OH

# Interaction Forces Due to Concentric Misalignment of Inner PF Coils with Respect to the OH Coil using the NTFTM Code

NTFTM2 is a mesh generation code with some capabilities to calculate magnetic fields and forces. It is used here partly to provide a check of the MAXWELL modeling and partly to support qualification of the NTFTM code as used in ref [1] and elsewhere. The MAXWELL OH PF1a,b force calculations are duplicated.

Load in Newton, Between thePF1a, and b grouped together and the OH as a function of Shift in mm  - MAXWELL (Ali Zolfaghari)  - NTFTM (Titus)

# Lateral Structural Stiffness - Bellows and Cantelevered Centerstack Casing

A portion of the global model [1] was extracted to obtain an estimate of the structural lateral stiffness. The model is shown below, and  the results of the analysis are shown in the following Figure:

The bellows detail in this analysis is old and could be updated to be consistent with ref [4], but the margins are large and the small change in bellows stiffness will not alter the conclusions of this calculation.

Compliance of the Belleville Spring Preload System.

The lateral stiffness of this assembly is complex,  but a major contributor is the cantelevered posts that center the Bellevilles. These are simply represented by 14 cantilevered  beams.

The lateral stiffness of the posts is 131 MN/m (see below) The combined bellows and post stiffness is (1/K bellows + 1/K Belleville posts)^-1  or (1/131+1/425)^-1= 100 MN/m

| Num of Spring Stacks | 14 |  |
| --- | --- | --- |
| Post Diameter | 1.2 | inches |
| Post Mom of Inertia= | -0.08482 | inches^3 |
| Post Height, L= | 5.2 | Inches |
| Modulus |  | 2.95E+07 |  |
| Bend Stiff per Post | -5.34E+04 |  |
| Bend Stiff all Posts | -7.47E+05 | lbs/in |
| Bend Stiff All Posts | -1.31E+02 | MN/m |