NSTX

Analysis of the NSTX Upgrade Centerstack Support Pedestal

NSTXU-CALC-12-09-00

Rev 0

May 2011

Prepared By:

___________________________________

Peter Titus, PPPL Mechanical Engineering

Reviewed By:

________________________________________

Ali Zolfaghari PPPL Mechanical Engineering

Reviewed By:

_______________________________________

Mark Smith, Cognizant Engineer

PPPL Calculation Form

Calculation # 	NSTXU-CALC-12-09-00    Revision #  00		WP #, 1672

(ENG-032)

Purpose of Calculation: (Define why the calculation is being performed.)

To qualify the stresses in Pedestal support for the centerstack assembly. Additionally, the effect of teh torsional stiffness of the pedestal will be assessed.

References (List any source of design information including computer program titles and revision levels.)

Included in the body of the calculation

Assumptions (Identify all assumptions made as part of this calculation.)

Calculation (Calculation is either documented here or attached)

See the following report

Conclusion (Specify whether or not the purpose of the calculation was accomplished.)

Stress levels in the support satisfy the  NSTX CSU criteria. Torsional stiffness of the pedestal has minimal effect on the torsional shear stress in the TF inner leg.

Cognizant Engineer’s printed name, signature, and date

Mark Smiuth

I have reviewed this calculation and, to my professional satisfaction, it is properly performed and correct.

Checker’s printed name, signature, and date

# 2.1 Table of Contents

NSTX Centerstack Pedestal

Section.Paragraph

Title Page                          	         							1.0

Table Of Contents                            							2.1

Revision Status Table                        						2.2

Executive Summary								3.0

Digital Coil Protection System Input						4.0

Design Input, 									5.0

Criteria                             							5.1

Design Point Spreadsheet Loads						5.2

References                                   						5.3

Analysis Model									6.0

Model elements								6.1

Materials and Allowables                     						7

Bolt Capacities                          						7.1

Fatigue Data

Stand-Alone-Model Results							8.0
	Normal Operating Downward Loads					8.1

Faulted Downward Loads							8.2

Normal Operating Upward Loads						8.3

Faulted Upward Loads							8.4

Global Model Results								9.0

deadweight								9.1

Normal Operating Loads Including Torsional Effects				9.2

Seismic Loads								9.3

3.0 Executive Summary:

The pedestal is a structure that provides gravity support for the centerstack and resists Coil Lorentz loads during operation..  Because it is connected to ground, the lower lid assembly, and the TF flags, and the skirt which supports the centerstack casing, it also is a contributor to the torsional stiffnesses that determine the distribution of the global torques in the machine. The pedestal must allow access to the service connections at the lower end of the centerstack. Provision must be made to allow passage of coolant lines, power leads and diagnostics. In order to service these lines, the pedestal may have to be able to be disassembled in pieces that do not capture the service connections.  The current design for the FDR is shown in figure 3.0-1. The number of bolts at the mid flange is 6 pairs - but this was described as needing resolution in an email from Mark Smith[10]. The analysis model uses four bolts in a pattern around the vertices of the trusses for a total of 8 pairs.  Shimming of the mid flanges is assumed to also align with the vertices of the trusses. Use of high strength bolts at the flange connections (Mid height and at the base) allows these connections to be capable of resisting the worst case power supply loads. The limit to the upward loading is the concrete anchors or Hilties. Ninety four 3/4 inch Hilties are required to resist the worst case power supply loads. It is not likely that this number will be used. Only five 3/4 inch anchors are needed to react the normal operating net load on the centerstack. Many more than 5 are suggested. This number will set the limit that must be maintained by the DCPS.

There have been a couple of design concepts proposed for the pedestal. During the CDR, the pedestal was a bolted plate assembly. A number  of analyses were performed based on this configuration, and the gusseted plate design was acceptable.  Designers were concerned that a torsionally stiffer structure was needed, although the analyses (which also had a stiff lower lid structure) did not show this.

Figure 3.0-2 Two Concepts Proposed for the Pedestal; "Vee" Pipe (Left) and Gusseted Plate (Right)

Aside from qualifying the present Vee-tube structure , the global model used for the inner leg torsional shear calculation has been run with both the plate and vee-tube structure.

Figure 3.0-3 Inner Leg Torsional Shear For Two Pedestal Concepts

After reviewing a few scenarios, there is no difference in the max TF inner leg torsional shear of 25 MPa, but there is a difference in the shear in the lower end of the TF inner leg. This implies that there is a difference in torques transmitted via the TF flags and crown to the pedestal and lower spoked lid. For both these components, the torques have been based on an upper bound for the upper connections which have been found to be larger. So it is likely that the re-distribution of torque that is caused by the "Vee" Pipe pedestal will not be a problem, but rigorously, these should be re-investigated for the chosen pedestal design.

Figure 3.0-4 PDR Summary of Pedestal Designs

Figure 3.0-4 shows the work performed on the pedestal up  to the PDR . The gusseted plate design has upper "vanes"  that are torsionally weak and appear weak with respect to side loads from seismic and halo loads, but  their stresses are well within allowables. . Stresses in the "Vee" pipe truss pedestal design are slightly lower than for the gusseted plate design. Both are less than 20 MPa for normal loads and less than 200 MPa for the faulted loads. This provides a large margin. The bending allowable is  241 MPa for 316 weld material. Assuming full penetration welds producing no stress multiplier on the stress that is reported by the FEA analyses, the welds and structural elements have a large margin against normal loads and a normal design  margin for faulted loads. . Connection to the TF flags is discussed, in Ali Zolfaghari's calculation [9]

The seismic analysis [6] was checked for the "Vee"  pipe design - most of the modeling was with the plate design- and the seismic stress levels in the pedestal are acceptable.

4.0 Digital Coil Protection System Input

Conceptual design of the upgrade to NSTX explored designs sized to accept the worst loads that power supplies could produce. Excessive structures resulted that would have been difficult to install and were much more costly than needed to meet the scenarios required for the upgrade mission, specified in the General Requirements Document (GRD).  Instead the project decided to rely on a digital coil protection system (DCPS). For the pedestal the critical loads are the  vertical loads from the OH and PF1 a and b Upper and Lower coils interacting with the rest of the PF system. For the "Vee"  Pipe design torsional loads are added to the vertical loads. For the downward loads from the PF coils, both pedestal designs are adequate even for the "worst case power supply" loads.

The limit to the upward loading is the concrete anchors or Hilties.  Ninety four 3/4 inch Hilties are required to resist the worst case power supply loads. It is not likely that this number will be used. Only 5 3/4 inch anchors are needed to react the normal operating net load on the centerstack. Many more than 5 are suggested. The actual number will set the limit for the DCPS.

5.0 Design Input,

5.2 Design Point Spreadsheet Loads

5.3	References

[1] NSTX Structural Design Criteria Document, NSTX_DesCrit_IZ_080103.doc I. Zatz

[2] NSTX-CALC-13-001-00 Rev 1  Global Model – Model Description, Mesh Generation, Results, Peter H. Titus  March  2011

[4] NSTX Design Point Sep 8 2009  http://www.pppl.gov/~neumeyer/NSTX_CSU/Design_Point.html

[5] OOP PF/TF Torques on TF , R. Woolley, NSTXU CALC 132-03-00

[6] NSTX Upgrade Seismic Analysis NSTXU-CALC-10-02-00 Rev 0  February 9  2011 Prepared By: Peter Titus,

[7] "General Electric Design and Manufacture of a Test Coil for the LCP", 8th Symposium on Engineering Problems of Fusion Research, Vol III, Nov 1979

[8] "Handbook on Materials for Superconducting Machinery"  MCIC- HB-04  Metals and Ceramics Information Center, Battelle Columbus Laboratories 505 King Avenue Columbus Ohio 43201

[9] NSTX Upgrade TF Flag Key Structural Analysis, Calculation number NSTXU 132-08-00 prepared by Ali Zolfaghari

[10] Email from Mark Smith:

Pete,

Below is a more detailed image of the pedestal design.

There are two sections: upper and lower.

There are 6 (bosses or pads) between the upper and lower sections as well as the lower section and grout plate.Also, shims will be placed between the upper and lower sections.Thus, there are gaps between these components.Also note, the structural tubing was aligned as you mentioned.

However, the tubes are not aligned with all of the bosses. This needs to be resolved.

So, it will take some time to develop the CAD model for the FEA with some of these details.

Hopefully, this will be completed by next week.

Note:

The bolt sizing, spacing, total number required and preload have not been determined.

These details were scheduled for the final design analysis.

6.0 Analysis Model

The Pedestal is analyzed with two modeling approaches. It is included in the global model [2] and separate models of the pedestals are employed.  Two designs have been evaluated. One which was chosen for the  CDR and PDR analysis, uses gusseted plates. The second, introduced at the PDR and chosen for the FDR employs a trussed pipe design which is intended to be torsionally stiff. The pipe design basically has four stress areas at the pipes' intersection with the flanges. The gusseted plate design has six sets of gusseted plates which act as columns and flex plates (for torsion). The "Vee" Pipe  design has two versions - one which is linear and is included in the global model and another version that models with a gapped interface, the shims planedd to be placed between the mid height flanges to align the pedestal with the floor and centerstack elevations.

Figure 6.0-1 "Vee" Pipe model  The pads modeling the bolts were repositioned, and an inner and outer bolt circle is used.

Figure 6.0-2 "Vee" Pipe models -Misaligned and Aligned

The first evolution of the Vee Pipe concept had "Vee" vertices misaligned at the mid plane where ideally, the compressive load should have been transferred directly without any offset and should not have required any plate bending to transfer the load. This was corrected in later versions of the design.

Figure 6.0-3 Ref 2 Global Model Udate with "Vee" Tube Pedestal

7.0 Materials and Allowables

Table 7.0-1Tensile Properties  for Stainless Steels

| Material | Yield, 292 deg K (MPa) | Ultimate, 292 deg K (MPa) |
| --- | --- | --- |
| 316 LN SST | 275.8[7] | 613[7] |
| 316 LN SST Weld | 324[7] | 482[7] 553[7] |
| 316 SST Sheet Annealed | 275[8] | 596[8] |
| 316 SST Plate Annealed |  | 579 |
| 304 Stainless Steel (Bar,annealed) | 234 33.6ksi | 640 93ksi |
| 304 SST 50% CW | 1089 | 1241 180ksi |

Table 7.0-2 Coil Structure Room Temperature (292 K) Maximum Allowable Stresses, Sm = lesser of 1/3 ultimate or 2/3 yield, and bending allowable=1.5*Sm

| Material | Sm | 1.5Sm |
| --- | --- | --- |
| 316 Stainless Steel | 184 | 276 |
| 316 Weld | 161 | 241 |
| 304 Stainless Steel (Bar,annealed) | 156MPa(22.6ksi) | 234 MPa (33.9ksi) |

ASTM A193 Bolt Specs from PortlandBolt.com

| B8M | Class 1 Stainless steel, AISI 316, carbide solution treated. |
| --- | --- |
| B8 | Class 2 Stainless steel, AISI 304, carbide solution treated, strain hardened |
| B8M | Class 2 Stainless steel, AISI 316, carbide solution treated, strain hardened |

## Mechanical Properties

| Grade | Size | Tensile ksi, min | Yield, ksi, min | Elong, %, min | RA % min |
| --- | --- | --- | --- | --- | --- |
| B8 Class 1 | All | 75 | 30 | 30 | 50 |
| B8M Class 1 | All | 75 | 30 | 30 | 50 |
| B8 Class 2 | Up to 3/4 | 125 | 100 | 12 | 35 |
|  | 7/8 - 1 | 115 | 80 | 15 | 35 |
|  | 1-1/8 - 1-1/4 | 105 | 65 | 20 | 35 |
|  | 1-3/8 - 1-1/2 | 100 | 50 | 28 | 45 |
| B8M Class 2 | Up to 3/4 | 110 | 95 | 15 | 45 |
|  | 7/8 - 1 | 100 | 80 | 20 | 45 |
|  | 1-1/8 - 1-1/4 | 95 | 65 | 25 | 45 |
|  | 1-3/8 - 1-1/2 | 90 | 50 | 30 | 45 |

Figure 7.0-3 Fatigue S-N Curve for 316 Stainless Steel

8.0 Stand-Alone-Model Results

The Pedestal is analyzed with two modeling approaches. In the "stand-alone" model, the pedestal model is separated from other structures and loaded via displacement constraints. An initial guess is imposed and then the displacement is scaled based on the resulting reaction forces to obtain the vertical loading specified by the design point spreadsheet.

Figure 8.0-1 Displacement Constraints on the Gusseted plate model

8.1 Normal Operating Downward Loads					8.1

8.2 Faulted Downward Loads

Downward and Normal and Faulted Stresses are acceptable for both pedestal concepts. Stresses are almost the same for both concepts.

8.3 Normal Operating Upward Loads

8.3.1 Pipe and Plate Stresses for Normal Operating Upward Loads

8.3.2 Bolting and Embedment Anchors for the Normal Operating Upward Loads

The analysis model uses four bolts in a pattern around the vertices of the trusses. Also shimming of the mid flanges is assumed to also align with the vertices of the trusses. Bolt sizes are assumed to be 1 inch diameter ASTM A 193 B8 bolts with an 80 ksi yield.  One inch bolts.6051 in stress area and thus the total upward capacity of the mid flange connection is 16*80000*.6051 = 774528 lbs. which is above the worst power supply load of 375500 lbs. So the flanges are readily made capable of resisting the faulted upward tensile load

8.4 Faulted Upward Loads

Figure 8.4-1 Vertical Displacements With Max Power Supply Loads Applied.

In figure 8.4-1,  the displacement profile shows the lift-off at the gap elements that model the shims under the Vee vertices.

Selection of high strength bolts allows at least the flanges to be capable of supporting the worst case power supply loading of the centerstack  of 375500 lbs.  Bolt sizes are assumed to be 1 inch diameter ASTM A 193 B8 bolts with an 80 ksi yield.  One inch bolts.6051 in stress area and thus the total upward capacity of the mid flange connection is 16*80000*.6051 = 774528 lbs. which is above the worst power supply load of 375500 lbs. So the flanges are readily made capable of resisting the faulted upward tensile load

Upward  Normal and Faulted Stresses are acceptable for both pedestal concepts. Stresses are similar for both concepts.

9.0 Global Model Results

Ref [2] describes the global model of the tokamak that was updated with the Vee tube pedestal in run#28. This analysis provides results for a number of load cases not readily available from the design point spreadsheet[4] .  The design point spreadsheet provides only axisymmetric loads from the PF coil currents.

9.1 Deadweight

Figure 9.1-1 Deadweight Stresses in the Pedestal

9.2 Normal Operating Loads

Figure 9.2-1 Scenario 13 "Vee" pipe Pedestal Stresses

Note that the Stresses in the "Vee" truss are not equal - this is an indication that some portion of the machine global torque is being transmitted into the truss.

Figure 9.2-2 Scenario 13 Gusseted Plate Pedestal Stresses

Figure 9.2-3 Scenario 14 "Vee" Pipe Pedestal Stresses

Figure 9.2-4 Scenario 15 "Vee" Pipe Pedestal Stresses

9.3 Seismic Loads

Seismic analysis of NSTX may be found in Reference [6], based on the global model analysis described in  reference [2]. Both of these calculations - as of May 2011- were based on the earlier gusseted  plate pedestal concept. The global model was re-run with the .5 g lateral load applied which is representative of the seismic response based on the more elaborate response spectra modal analysis also included in reference [6]

Figure 9.3.1

Figure 9.3-2 Secti

Figure 9.3-3 Plate Gusset Pedestal Seismic Stresses From Reference [6]

The seismic stresses in the pedestal are modest for both pedestal concepts.

# Text boxes

Figure 3.0-1  "Vee" Pipe Pedestal Evaluated for the FDR

Figure 3.0-5 Representative Pedestal Stress for the Worst Case Power Supply Loads